Towed Parachutist:

Pilot Lower Gear and 100% flaps (paratroop door drops only) Maintain min of drop Alt and airspeed avoid flying over or upwind of water or built up areas Shallow coordinated turns away from the parachutist CP - Red Light “ON”

LM Inform Pilot and have the jumpmaster stop the remaining jumpers Jumpmaster or safety will determine entanglement and make a recommendation via LM Priority: paratroop door – retrieve; ramp and door - cut if conscious (AC final authority)

CDS Malfunction:

Pilot Extend additional flaps as required (Tech – to the horn… 70%) Lower nose to slight nose low (don’t over control) Maintain drop altitude and airspeed, avoid flying over or upwind of built up areas and water CP – Red Light “ON”

LM De-arm CDS switch Notify pilot of malfunction Alert parachutists to stay forward/clear of the load (if req’d) Raise aft anchor supports (if required) Clearance to close ramp and door (if jammed in ramp area stop closing action when released from up-lock) Secure load – completion of drop checklist When dropping double stick using CVR, LM will delay notifying the pilot until both sticks have exited the aircraft

Heavy Equipment Malfunctions:

Pilot (all situations) Maintain drop altitude and airspeed Avoid flying over or upwind of water or built up areas CP - Red light “ON”

LM (extraction chute fails/falls or loose platform) Notify pilot of malfunction Alert parachutists to stay forward/clear of the load (if req’d) Emergency aft restraint (fwd to aft) Raise aft anchor supports (if required) Clearance to close ramp and door Re-lock and secure platform – completion of malf/drop checklist

LM (single parachute outside) Notify pilot of malfunction (after pulling right hand emergency handle) Alert parachutists to stay forward/clear of the load (if req’d) Emergency aft restraint (fwd to aft) Cut aft of the attachment point Raise aft anchor supports (if required) Clearance to close ramp and door Re-lock and secure platform – completion of malf/drop checklist

LM (multiple 28 ft fail/fall) Notify pilot of malfunction Alert parachutists to stay forward/clear of the load (if req’d) Raise aft anchor supports (if required) Clearance to close ramp and door Re-lock and secure platform – completion of malf/drop checklist

LM (multiple 28’ outside aircraft) Pull right hand emergency handle Left hand Simul handle (10-20 seconds steady pull for stuck locks) Notify pilot and brace for impact NOTE: Pilot - max power, no slower than VMETO speed, look for a place to land